Quantifying the Non-Existent
Multi-wavelength Model Fitting
with Non-Detects
Tanmoy Laskar
Ph.D. Student in Astronomy
Harvard University

---
Outline
- Context – Gamma Ray Bursts and their Afterglows
  - The Phenomenon
  - Light Curves and Modeling
- Radio Interferometry
  - Visibilites and The van Cittert – Zernike Theorem
  - Deconvolution
  - The Measurement Process
- Incorporating Non-detects

---
Gamma Ray Bursts
Γ ~ 102-103
Γ ~ 10

---
GRB Lightcurves
- Light curve = Fn(t)
- Afterglow first appears in X-rays
- Peak emission moves to lower frequencies with time
Laskar et al. (in prep.)
color white {M(widevec {P} ) = F_M({%nu},t)}

---
Multi-wavelength modeling
Laskar et al. (in prep.)
color white {M(widevec {P} ) = F_M({%nu},t)}
Frail et al. (2006)

---
Radio Interferometry
color white {V(u,v) = lim from{T rightarrow infinity} to {} {{1} over {T}} int E_1 (t) E_2(t) dt}
color white {V(u,v) = int I(%alpha,%beta)e^{2%pi i(u%alpha + v%beta)} d%alpha d%beta}

---
Measuring V(u,v)
color white {V_m(u,v) = W(u,v)V(u,v)}
color white {IFT (V_m(u,v)) = IFT(W)*IFT(V)}
color white {{}= B(%alpha,%beta)*I(%alpha,%beta)}

---
Deconvolution
The CLEAN Algorithm:
  - Find map max
  - Subtract (gain x dirty beam at position of peak) from map
  - Add d-function to clean components list
  - Repeat
1. "Dirty image" = IFT Vm
2. Clean: obtain clean components and residuals
3. Restore: convolve cc with "clean beam" and add back residuals
Hogbom (1974)

---
Detection?
- Fit the source with the known clean beam (elliptical Gaussian)
- Obtain source parameters (shape, size), both convolved with and deconvolved from clean beam
- Non-detect? Report upper limit = 3 x rms of map …

---
Model Fitting – Maximum Likelihood
xi : detected values
ci : upper limits
color white {t_i = min(x_i,c_i)}
color white {%delta_i = left lbrace binom {0 " (censored)"} {1 " (detected)"} right none}
color white {L = prod from i=1 to N P[t_i,%delta_i] = prod from i=1 to N left [f(t_i) right]^{%delta_i} left [1-S(t_i) right]^{1-%delta_i}}
color white {f(x) = 1 over {sqrt{2%pi}%sigma} e^{(x-%mu)^2 over {2%sigma^2}}}
color white {S(x) = 1- 1 over 2 left [1+erf left ({x-%mu} over {sqrt 2 %sigma} right ) right]}