## Slide 1: The X-Ray Imaging and Spectroscopy Mission
Richard Kelley
NASA Goddard Space Flight Center
Memorial Symposium to Honor
Riccardo Giacconi
Washington, DC
29-30 May 2019
Chandra image
Hitomi/SXS spectrum

## Slide 2
X-ray emission from clusters of galaxies was first detected by Gursky et al., 1971 in the Uhuru X-ray sky survey
  Extended (~45 arcmin) source found associated with the Coma cluster.
Similar extended cluster X-ray sources were later discovered (e.g. Perseus, Virgo), but the spectra at the time were insufficient to distinguish between power law and thermal bremsstrahlung spectra.
Two possible mechanisms were proposed:
  Inverse Compton radiation from 3 K microwave background photons interacting with a relativistic electron population in the cluster (Brecher and Burbidge, 1972).
  Thermal bremsstrahlung from a hot isothermal gas (Lea et al., 1973).
Discovery of X-ray Emission from Clusters of Galaxies
Fe K emission

## Slide 3
Expected X-ray spectrum of intra-cluster medium

## Slide 4
X-Ray Calorimeter (1982)
Energy resolution of ~ 1 eV theoretically possible

## Slide 5
The AXAF X-Ray Spectrometer (XRS)
≈ 140 eV resolution

## Slide 6: The “XRS” is History!
AXAF
Chandra
AXAF-I AXAF-S
AXAF
Astro-E
Astro-E2
Astro-H
XRISM
1993
2000
2005
2016
2022

## Slide 7
SXS – energy resolution better than 4.9 eV at system level
6 x 6 array of 30” x 30” pixels (3 arcmin FOV)
Soft X-Ray Telescope
5.6 m focal length – fixed optical bench
203 concentric shells (1624 individual reflectors)
Outer Diameter: 45 cm
Mass: CBE = 46 kg.
Half-Power Diameter of better than 1.2 arcmin
NASA Hardware Contributions to Astro-H
Soft X-Ray Spectrometer

## Slide 8
1st Astro-H target – Perseus Cluster
(Chandra image, Fabian et al.)
Astro-H launch
Feb 17, 2016 JAXA HII-A

## Slide 9
3 arcmin ~ 60 kpc
1st Astro-H target – Perseus Cluster
(Chandra image, Fabian et al.)

## Slide 10: Astro-H (Hitomi) SXS Spectrum of Perseus cluster
BLACK: Hitomi SXS (energy resolution 4.9 eV, FWHM)
BLUE: Best previous spectrum (Suzaku CCD; FWHM 140 eV)
Hitomi Collaboration, Nature 2016

## Slide 11: Astro-H (Hitomi) SXS Spectrum of Perseus: He-like Fe
BLACK: Hitomi SXS data
PURPLE: Hitomi SXS line response function
BLUE: Best previous spectrum (Suzaku CCD)
σturb = 164 ± 12 km s-1
Pturb < 0.04 x Pthermal
Energy (keV)
Hitomi Collaboration, Nature 2016
Notice how the high spectral resolution of Hitomi/SXS allows easy detection of the turbulent velocity broadening. This capability was eagerly anticipated for all nearby clusters.

## Slide 12
The X-Ray Imaging and Spectroscopy Mission
X-Ray Mirror Assemblies (2)
Coming in 2022
Incorporates many lessons learned from Astro-H
Resolve X-Ray Spectrometer
Xtend CCD Imager

## Slide 13: US Access to XRISM
NASA to have access to ~ 44% of observing time and all data from Resolve and Xtend once in US archive (+1 year). JAXA and ESA have separate agreement on remainder.
NASA responsible for data pipeline and dissemination.
NASA Participating Scientists selected by NASA (science advisors):
  Lia Corrales/U. Michigan Erin Kara/MIT Jon Miller/U. Michigan
  Paul Plucinsky/SAO Irina Zhuravleva/U. Chicago
Additional target Collaborating Scientists to be selected to support performance/verification phase (6 months duration following commissioning)
It is anticipated that ~ 60 scientists will be selected to join target teams.
AO for Collaborating Scientists to be released in late 2020.
Negotiating early release data from a few targets shortly after commissioning.
AO-1 released after commissioning (~ late Spring, 2022).

## Slide 14
Giant leap: ATHENA will push capability all the way out to z ~ 1
Contains very large fraction of all x-ray clusters
3168-pixel array, 2.5 eV resolution
Memorial Symposium to Honor Riccardo Giacconi
14